## Slide 1: ERL TITLE
Author | Date
Subtitle

## Slide 2: Contents
1
Template Layouts
2
3
5
4
Campus Sub-brand Logos
Fonts
PowerPoint vs Keynote vs Google Slides
Slide Examples

## Slide 3: Background

## Slide 4: Probability Basics
Sample Space
Probability Measure
Probability Space

## Slide 5: Conditional Probability & Independence
Conditional probability
  If we know Event B is true, what is the probability of Event A occurring?
Bayes Rule
likelihood
posterior
prior
Assume P(B) > 0
Notes: Bayes Rule provides a relationship between the conditional probability mass functions and the marginal probability mass functions of 2 random variables m and z joint pmf of M and Z is p(m,z)) Bayes Rule allows us to switch the order of the r.v. in the conditionals

## Slide 6: Bayes Rule
Joint PMF
Marginal PMF
Conditional PMF
Total Probability

## Slide 7: Probability Basics
Discrete Random Variable
Cumulative distribution function
Probability distribution function/probability mass function

## Slide 8: Frames and Transformations
Red - global frame
Yellow - robot frame
(0,0)
(0,0)

## Slide 9: Frames and Transformations
Vector <a,b>
Angle θ
2D Rotational Matrix
Translational Vector
Vector in global frame (output)
Vector in robot frame (input)

## Slide 10: Occupancy Grid Mapping

## Slide 11: Occupancy Grid Map Scenario
Global position of the robot
Range sensor (LiDAR scans)
Map of explored environment with obstacles
Goal: Build a map of the environment
Knowns
Unknowns
Probability density function for the map (m) given the sensor measurements (z) and robot positions (x) from time=1 to time=t

## Slide 12: Occupancy Grid Map Scenario
m - entire map space
zt - sensor measurements at time t
xt - robot position at time t
mi - map grid cell

## Slide 13: Grid Discretization
Continuous Space
Discrete Space
mi - space of one grid cell
m - space of map space
n - number of grid cells

## Slide 14: Occupancy Grid Map
mi - space of one grid cell
Each mi can have a binary state of 0 or 1
  Free space represented by mi = 0
  Occupied space represented by mi = 1
Goal: want to know p(mi = 1) or p(mi), probability of the grid cell mi is occupied (mi = 1) to approximate the map m

## Slide 15: Occupancy Grid Map
Each mi is independent from mj (where i ≠ j)
  If you don’t check mi, there is no way to know the state of mi based on knowing mj (where i ≠ j)
  Even if you know what neighboring cell states are, you cannot predict the state of mi using occupancy grid mapping
Independence between cells simplifies the problem
  Only need to track individual cell info, not relations/connections between cells
mi - space of one grid cell

## Slide 16: Occupancy Grid Map
p(mi) - probability that this grid cell is occupied
p(mi | z0:t , x0:t) - probability that the grid cell mi is occupied, 0<= p(mi | z0:t , x0:t) <=1
Can adjust p(mi | z0:t , x0:t) based on:
  z0:t - measurements from our sensor (taken at a certain time) that detect whether there is an object occupying that space
  x0:t - positions of our robot at different times (robot trajectory) that include global position coordinates and orientation of the robot

## Slide 17: Bayes Rule and Mapping
We will call our pmf γi,t
Apply Bayes rule (w/ cond. prob.)
Simplify w/ Markov assumptions
Create recursive definition for γi,t
ph is a label so we can reference this pmf more easily

## Slide 18: Bayes Rule and Mapping Complement
We want to write a similar recursive expression for p(mi = 0 | z0:t , x0:t )
Apply definition of a complement
Use recursive definition for γi,t found on previous slide

## Slide 19: Mapping and Odds Function
Apply definition of a complement
Expand using relations from previous two slides
Define a function σ(E) = p(E) / (1 - p(E))
Use relations from previous two slides
Recursive definition for σ(E) gh(zt | mi , xt ) is the updating factor

## Slide 20: Mapping and Log-Odds Function
Use definition of σ(E) from prev slide
Recursive definition of λ(E)
Explicit definition of λ(E) where λ(mi) is the log-odds of the initial probability of mi being occupied before any measurements

## Slide 21: Mapping and Log-Odds Update
Here we simplify notation by defining λi,t
We rewrite the recursive definition of our log-odds function here.
We want to determine how to calculate the change in λi,t (update from previous log-odds to new log-odds)

## Slide 22: Inverse Sensor Model Concept
True Positive - sensor detects an occupied cell when the cell is occupied
False Positive - sensor detects an occupied cell when the cell is free
False Negative - sensor detects a free cell when the cell is occupied
True Negative - sensor detects a free cell when the cell is free
We can define our sensor model by defining these four probability values, can be obtained experimentally or defined theoretically.

## Slide 23: Inverse Sensor Model (Log-odds Update)
Use definition of gh from “Mapping & Odds Function”
Expand with Bayes Rule
Simplify with Markov assumption
Substitute with previous definition of λ(mi)
gh tells us how likely our measurement if we know the map occupancy state and robot position

## Slide 24: Occupancy Grid Mapping Summary
If we start with some initial λi,0, , then we can use this relation to update the λi (log-odds value of map cell mi) for every time step until we reach λi,t.
We have now rewritten the recursive relationship in a more useful form.
The previous form included gh (zt | mi , xt), which depends on knowing the state of mi the exact value we are trying to determine.

## Slide 25: Initial Log-Odds Value
If we have no information about cell mi
then we can choose to assume there is equal likelihood of mi being occupied and of mi being free. λ(mi) = 0
What is the initial log-odds value of the cell mi before we have taken any measurements with our robot?
If we are optimistic about cell mi being occupied (without measuring anything), then λ(mi) can be greater than 0. If we are optimistic about cell mi being free, then λ(mi) can be less than 0.

## Slide 26: Implementation

## Slide 27: Probability as Log-Odds
Using log-odds instead of probabilities removes the potential rounding errors for floats close to 0 or 1
Probability ➝ Log-odds
Log-odds ➝ Probability
Log-odds l(x): (-inf, inf)
Probability p(x): [0,1]

## Slide 28: Bresenham’s Algorithm Introduction
Describes a way to take a continuous line segment/vector and graphically represent it using pixels
Helpful for mapping because we take a LiDAR ray (continuous line segment) and want to know which grid cells (pixels) it passes through

## Slide 29: Bresenham’s Algorithm Intuition
For every 1 unit increase in y
Which x-value (x0 or x0+1) is closer to the continuous value y(x)?
If x0 is closer to y(x), choose (x, y) as our pixel, otherwise choose (x0+1, y) as our pixel.
Keep repeating until we reach end point
(1,1)
(6,8)

## Slide 30: Bresenham’s Algorithm Scenarios
(1,1)
(6,8)
(1,1)
(8,6)
m > 1, want to increment by y and compare x values
m < 1, want to increment by x and compare y values
In general, the x or y direction with the greater change is used as the increment by 1 direction.

## Slide 31: Bresenham’s Algorithm
Algorithm Bresenham (x1, y1, x2, y2) {
x = x1; y = y1;
dx = x2 - x1; dy = y2 - y1;
p = 2*dx - 2*dy // indicates the closer y value while ( x < x2) {
add (x,y) to pixel_list
x++;
if ( p<0 )
p = p + 2*dy;
else
p = p + 2*dy - 2*dx;
y++;
}
}
Bresenham (1,1,8,6)
(1,1)
(8,6)

## Slide 32: Bresenham’s Algorithm Notes
Where did the derivation of p come from? Reference
  Remember we can find the closer value by plugging in y(x0) and y(x0+1) and pick the closer one found from y = mx+b
  Derivation comes from manipulation of y=mx+b and m = y/x —> why manipulate? To avoid using floats (calculation inaccuracies, more expensive operations)
How would you use Bresenham’s algorithm for vectors in different quadrants?
  E.g. positive dx and positive dy vs. negative dx and positive dy scenarios

## Slide 33: Occupancy Grid Mapping Pseudocode

## Slide 34: Occupancy Grid Mapping Examples

## Slide 35: Occupancy Grid Map
Fig.2.2 Occupancy grid map from sample data
Fig.2.1 Occupancy grid map

## Slide 36: Occupancy Grid Map Simulation
Fig.2.4 Log-odds map from example
Fig.2.3 Simulation Example

## Slide 37: Bresenham’s Algorithm
(1,1)
(6,8)
(1,1)
(6,8)

## Slide 38: Sensor Model
Models allow us to connect our specific robot behaviors/attributes to the general algorithm.
xt (robot positions) and zt (sensor measurements) used to update mi (any grid cell).
Things that can affect chosen sensor model: type of sensor (e.g. LiDAR), sensor position on robot, etc.

## Slide 39: Thank you!